Preliminary Project Discussion for Sewage Works Construction Projects

Background Information

Engineer/ Owner

Project Name:	The Grove TF Section 11 (Collection Lines Only)

Eudaily Treatment Facility Williamson County

NPDES or SOP Number (if existing):

- Identification of parties

  - Applicant		Adenus

  - Permittee		Tennessee Wastewater Systems Inc (TWS Inc)

  - Consulting Engineer	Jamie Reed P.E., R.L.S.

  - Funding Agencies (if applicable)	None

- Entity to sign off on compliance with local codes (i.e. building inspector)	TWS Inc

- Project Purpose and Objectives

The existing Boswell Tim’s Ford Treatment Facility is located at Boswell Road just north of Mansford Road. The Boswell Tim’s Ford Treatment Facility was built and approved with an effluent limit of 24,700 gpd. Existing installed items are as follows (58 ft x 96 ft) Recirculating Media Filter (RMF) Treatment System, 5,000-gal recirculation tank, control building and 14.63 acres of drip dispersal as the land application, 6 drip dispersal zones at 5,850 LF per zone, installed on the existing treatment facility property. This facility will be designed to serve the sewage needs of the Boswell Tim’s Ford service territory.

- Map of general service area (see attached service territory map)

  - Probable site and construction area see pdf of plans

  - Adjacent properties see pdf of plans

  - Significant waters of the State 	See PER

  - Geological features see pdf of plans

  - Property boundaries see pdf of plans

- Existing Inflow and Infiltration (see above) Proposed drip dispersal design flow 24,700 GPD

- Influent characteristics

  - Last 12 MORs (if applicable) 110,110 gpd exist flows

  - Industrial dischargers none

- System capacity

  - Hydraulic

    - Average Daily Dry Weather Flow – ADDWF

    - Average Daily Flow - ADF

    - Peak Flow	0.785 MGD

    - Design Flow	0.785 MGD

  - Nutrient

    - Influent loads

      - Average Daily Dry Weather Flow - ADDWF

      - Average Daily Flow – ADF 0.110 MGD

      - Design Flow 0.785 MGD

  - Treatment/ Conveyance

    - Accommodation of variability of loads drip dispersal no direct discharge

- Procurement methodology

  - Design-bid-build No

  - Design build No

  - Preselection of equipment/processes Adenus will install per construction plans

  - Relationships of various agencies involved Williamson County Planning (planning authority), Milcrofton Utility District, TDEC (approvals)

  - How and when ownership/access/easements will be transferred to wastewater operational entity currently exist

- Reliability class of components and electrical service

  - Operator certification level	TWS Inc

  - Manpower requirements	1 person

- Proposed project schedule projected start date Dec 2022

- Provide copy of PER if already prepared PDF sent