Preliminary Project Discussion for Sewage Works Construction Projects

Background Information

Engineer/ Owner

Project Name:

NPDES or SOP Number (if existing):

- Identification of parties

  - Applicant   Aqua Green Utility

  - Permittee   Aqua Green Utility

  - Consulting Engineer  Bob Fauhaber

  - Funding Agencies (if applicable) NA

  - Entity to sign off on compliance with local codes (i.e. building inspector) Williamson County

- Project Purpose and Objectives  Sewer works for Rec Center addition

- Map of general service area

  - Probable site and construction area  See Uploaded ER For Bethesda Subdivision Drip field locations will change  Tanks and equipment added to original location

  - Adjacent properties Rec Center for Williamson County

  - Significant waters of the State Un named Creek to West Harpeth River

  - Geological features Rolling farm land

  - Property boundaries see map

- Existing Inflow and Infiltration  NA

- Influent characteristics  Residential Sewage and Recreation Center

  - Last 12 MORs (if applicable)

  - Industrial dischargers

- System capacity 14,700 GPD + 18,490

  - Hydraulic  14,700 GPD + 18,490

    - Average Daily Dry Weather Flow - 14,700 + 18490

    - Average Daily Flow - ADF - 14,700 + 18490

    - Peak Flow

    - Design Flow

  - Nutrient  See Uploaded ER Subdivision

    - Influent loads

      - Average Daily Dry Weather Flow - ADDWF  Max 300 GPD per Home + 18,490

      - Average Daily Flow - ADF  Max 300 GPD per Home + 18,490

      - Design Flow  Max 300 GPD per Home + 18,490

  - Treatment/ Conveyance  STEG System to Lift station to treatment in Sealed PVC piping

    - Accommodation of variability of loads  Pump tank has extra holding 20 KW Diesel Back Up Generator will be used

- Procurement methodology

  - Design-bid-build   NA

  - Design build  Advanced Septic Builds then Aqua Green utility takes plant

  - Preselection of equipment/processes  Equipment selected on efficiency and existing utility use.

  - Relationships of various agencies involved  Advance septic and Aqua Green owned by Dart Kendall

  - How and when ownership/access/easements will be transferred to wastewater operational entity  Easements already signed.  Land ownership to utility before any work begins per contract with developer  Property has access to public road and electricity.

- Reliability class of components and electrical service

  - Operator certification level  BNS

  - Manpower requirements  PLC runs daily operation and service technician available via txt and Email anytime needed

- Proposed project schedule    Start June 2021 to start building Phase 1 Subdivision

  - Provide copy of PER if already prepared   See Uploaded ER for subdivision ER being prepared for Rec Center add on