TENNESSEE Department Of Environment And Conservation

Division of Water Resources

William R. Snodgrass Tennessee Tower, 312 Rosa L. Parks Avenue, 11th Floor, Nashville TN 37243

1-888-891-8332 (TDEC)

Compliance Inspection for General NPDES Permit for Stormwater Discharges from Construction Activities (CGP)

| Site/Project Name: | Bush Brothers & Company, Inc. | NPDES Tracking Number: | TNR133967 |
| --- | --- | --- | --- |
|  |  | Date Coverage was Issued | 15-JUL-11 |
| Street Address or Location: | 3304 Chestnut Hill Road | Start date: | 15-JUN-11 |
|  |  | Estimated end date: | 15-APR-12 |
| Site Description: | Demolish plant buildings and restore 1,600 feet of stream. | Latitude (dd.dddd): | 35.932602 |
|  |  | Longitude (-dd.dddd): | -83.339753 |
| County(ies): | Jefferson | EFO: Knoxville | MS4 Jurisdiction: |  | Acres Disturbed: | 0 |
|  |  |  |  |  | Total Acres: | 4.1 |

| Name of Permittee (Developer/Operator): Bush Brothers & Company, Inc. |
| --- |
| Name of Official Contact: Terry Dockery | Email: tdockery@bushbros.com | Contact Phone: 865-509-2304 |
| Address: 3304 Chestnut Hill Road | City: Dandridge | State: TN | Zip: 37725 |

| Check List (office & field checks) | Yes | No | Comments |
| --- | --- | --- | --- |
|  | Does the site have CGP coverage? | x |  |  |
|  | Is NOC posted on site? |  | x |  |
|  | Have the site contractors signed the NOI? | x |  |  |
|  | Is the current SWPPP available for review? |  | x |  |
|  | Are EPSCs in accordance with SWPPP? | x |  |  |
|  | Are EPSCs installed properly and functional? | x |  |  |
|  | Are inspection reports available on site? |  | x |  |
|  | Is the proper buffer zone maintained? | x |  |  |
|  | Were there unstable, inactive areas on the site? If so, does inspector know if length of time has been more than 14 days (or 7 days for steep slopes)? |  | x |  |
|  | Are more than 50 acres disturbed at one time? |  | x |  |
|  | Has sediment discharged off site? |  | x |  |
|  | Has sediment discharged into waters of the State? |  | x |  |
|  | Are there unauthorized alterations to waters of the State? |  | x |  |
|  | Are there violations of an existing ARAP? If so, ARAP No.? |  | x |  |
|  | Other pollutants/discharges or unusual problems? |  | x |  |
|  | Project is complete and stable with no construction-related stormwater discharges? | x |  |  |

| General Comments:project is complete and stable |
| --- |
| Routine |  | Comprehensive |  | Complaint |  | Follow Up |  | Termination | x |  |

| On-Site Contact (if available) |
| --- |
| On-Site Contact Name (Print): | On-Site Contact Title: | Signature: | Date: |

| TDEC Personnel/Information | EFO: Name and Address Knoxville Environmental Field Office 3711 Middlebrook Pike Knoxville, TN 37921 |
| --- | --- |
| Inspector’s Name (Print): Leigh Yates | Signature: | Date: 12/22/17 |  |
|  |  | Time: 1125 |  |